## Slide 1
Logic, Gates,
& Circuits

## Slide 2: ALERTs
Assignment 3 is due today
Lab 6 is due Monday
Assignment 4 is available on Brightspace and the course web site. It is due next Friday (9/27)

## Slide 3: What is Logic?
A logic statement is a sentence or assertion that can either be true or false
For example:
  "Abraham Lincoln was the last Czar of Russia"
  "I have three children"
  2 + 2 = 4
  x > 10
  t = "AATC" or (t = "TCCG" and s = "CTA")
  if mammal(X) then hasFur(X)
Statements can be combined by Boolean operators, like in the last two examples
Logic shows up in algorithms as the test conditions for if statements and while loops

## Slide 5: Physics Meets Logic
Transistors
  Solid-state switches
  Change on/off when given power on control line
  Extremely small (billions per chip)
  Enable computers that work with gigabytes of data

## Slide 7: Boolean Logic and Gates
Gate: an electronic device that operates on inputs to produce outputs
Each gate corresponds to a Boolean operator

## Slide 8: Boolean Logic and Gates
Gates are built from transistors
NOT gate: 1 transistor
AND gate: 3 transistors
OR gate: 3 transistors
NAND and NOR: 2 transistors

## Slide 11: Building Computer Circuits
Circuit: has input wires, contains gates connected by wires, and has output wires
Outputs depend only on current inputs: no state

## Slide 13: Building Computer Circuits
To convert a circuit to a Boolean expression:
  Start with output and work backwards
    Find next gate back, convert to Boolean operator
    Repeat for each input, filling in left and/or right side
To convert a Boolean expression to a circuit:
  Similar approach
To build a circuit from desired outcomes:
  Use standard circuit construction algorithm:
    e.g., sum-of-products algorithm

## Slide 14
Output =
x + y
y
p • q + y
p
q
x
m
m • b • q + y
~a • b • ~c + n • q
~a • b • ~c + y
n
~a • b • ~c + a • b • ~c

## Slide 16: Building Computer Circuits
Example from text
Build truth table:
a | b | c | Output1 | Output2
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0

## Slide 17: Building Computer Circuits
Example from text
Find true rows for Output1
a | b | c | Output1 | Output2
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0

## Slide 18: Building Computer Circuits
Example from text
For each true row AND inputs to make expression
  a = 0, b = 1, c = 0: (~a  b  ~c)
  a = 1, b = 1, c = 0: (a  b  ~c)
Combine row subexpressions with OR
  (~a  b  ~c) + (a  b  ~c)
Build circuit from expression
(and repeat for other output)

## Slide 21: ALERTs
Assignment 4 is available on Brightspace and the course web site. It is due Friday (9/27)
Lab 7 is now available on Brightspace. It is due next Monday (9/30)
The first midterm is Friday, October 4.

## Slide 22: Building Computer Circuits
Full adder circuit
Input is two unsigned N-bit numbers
Output is one unsigned N-bit number, the result of adding inputs together
Example:
Start with one-bit adder (1-ADD)
 |  |  |  | 1 | 
 | 0 | 0 | 1 | 0 | 1
+ | 0 | 1 | 0 | 0 | 1
 | 0 | 1 | 1 | 1 | 0

## Slide 24: Building Computer Circuits
Sum digit, si, has Boolean expression:
  (~ai  ~bi  ci) + (~ai  bi  ~ci) +
  (ai  ~bi  ~ci) + (ai  bi  ci)
Carry digit, ci+1, has Boolean expression:
  (~ai  bi  ci) + (ai  ~bi  ci) +
  (ai  bi  ~ci) + (ai  bi  ci)

## Slide 27: Building Computer Circuits
N-bit adder circuit
Input: a0a2…an-1 and b0b2…bn-1, where ai and bi are individual bits
a0 and b0 are least significant digits: ones place
Pair up corresponding bits: a0 with b0, a1 with b1, etc.
Run 1-ADD on a0 and b0, with fixed carry in c0 = 0
Feed carry out c1 to next 1-ADD and repeat

## Slide 29: Control Circuits
Control circuits make decisions, determine order of operations, select data values
Multiplexor selects one from among many inputs
  2N input lines
  N selector lines
  1 output line
Each input line corresponds to a unique pattern on selector lines
That input value is passed to output

## Slide 31: Control Circuits
Decoder sends a signal out only one output, chosen by its input
  N input lines
  2N output lines
Each output line corresponds to a unique pattern on input lines
Only the chosen output line produces 1, all others output 0

## Slide 33: Control Circuits
Decoder circuit uses
  To select a single arithmetic instruction, given a code for that instruction
  Code activates one output line, that line activates corresponding arithmetic circuit
Multiplexor circuit uses
  To choose one data value from among a set, based on selector pattern
  Many data values flow into the multiplexor, only the selected one comes out