## Slide 1
The Von Neumann Architecture

## Slide 2: ALERTs
Assignment 4 is due Friday.
Lab 7 is now available on Brightspace. It is due next Monday
Lab 8 is now available on Brightspace. It is due next Wednesday

## Slide 3: Excuse me, Can you tell me how to get to...
So, how do we build an entire computer out of gates?
  We don't, any more than we build one out of transistors...
  Abstraction!
  We will use a bottom-up approach to build functional units out of which a computer can be constructed.

## Slide 4: The Von Neumann Architecture
John Von Neumann
“If people do not believe that mathematics is simple, it is only because they do not realize how complicated life is.”

## Slide 5: The Von Neumann Architecture
John Von Neumann
John von Neumann (left) and Manhattan Project leader J. Robert Oppenheimer, in front of Princeton’s Institute for Advanced Study (IAS) computer

## Slide 6: The Components of a Computer System
Von Neumann architecture
Foundation for nearly all modern computers
Characteristics:
  Central Processing Unit (CPU)
    arithmetic/logic unit (ALU)
    control unit
  RAM: random access memory
  I/O: input/output
Stored program concept
Sequential execution of instructions

## Slide 8: Memory and Cache
Memory: functional unit for data storage/retrieval
Random access memory (RAM)
  Organized into cells, each given a unique address
  Equal time to access any cell
  Cell values may be read and changed
Cell size/memory width typically 8 bits
Maximum memory size/address space is 2N, where N is length of address

## Slide 9
1 KB = 1 kilobyte
  210 = 1024 ~ 103
1 MB = 1 megabyte
  220 = 1,048,576 ~ 106
1 GB = 1 gigabyte
  230 = 1,073.741,824 ~ 109
1 TB = 1 terabyte
  240 = 1,099,511,627,776 ~ 1012
1 PB = 1 petabyte
  250 = 1,125,899,906,842,624 ~ 1015
1 EB = 1 exabyte
  260 = 1,152,921,504,606,846,976 ~ 1018
1 ZB = 1 zettabyte
  270 ~ 1021
1 YB = 1 yottabyte
  280 ~ 1024

## Slide 11: Memory Circuits
The circuits we've seen so far have all be examples of what are called combinatorial circuits
  These perform computations that are functions of inputs to outputs
  These kinds of circuits can't be used to store data, since they are feeding signals in a forward path through the electronics
Sequential circuits are designed to store bits (0s and 1s) over time, so support operations that store and fetch
  Storing a 1 is called 'set'
  Storing a 0 is called 'reset'
  An SR-Flip Flop is a circuit that implements this idea

## Slide 12: SR-Flip Flop
S R | Q Q’
0 0 1 0 0 1 1 1 | Q Q’ 0 0 1 0 0
S R | Q Q’
1 1 0 1 1 0 0 0 | Q Q’ 0 0 1 1 1
RESET
SET
SET
RESET

## Slide 14: Memory and Cache (continued)
Fetch: retrieve from memory (nondestructive)
Store: write to memory (destructive)
Memory access time
  time required to fetch/store
  Modern RAM requires 5-10 nanoseconds
MAR holds memory address to access
MDR receives data from fetch, holds data to be stored

## Slide 15: Memory and Cache (continued)
Memory system circuits: decoder and fetch/store controller
Decoder converts MAR into signal to a specific memory cell
  One-dimensional versus two-dimensional memory organization
Fetch/Store controller = traffic cop for MDR
  Takes in a signal that indicates fetch or store
  Routes data flow to/from memory cells and MDR

## Slide 19: Memory and Cache (continued)
RAM speeds increased more slowly than CPU speeds
Cache memory is fast but expensive
Principle of locality:
  Values close to recently-accessed memory are more likely to be accessed
  Load neighbors into cache and keep recent there
Cache hit rate: percentage of times values are found in cache