## Slide 1
The CPU
(ALU & CU)

## Slide 2: ALERT
Assignment 4 is due today.
Lab 7 is now available on Brightspace. It is due next Monday
Lab 8 is now available on Brightspace. It is due next Wednesday
No new Homework this week: study for the midterm!
HW #5 will be available on Wednesday and due 10/11

## Slide 4: The Components of a Computer System The Arithmetic/Logic Unit
The ALU is part of the processor
It contains circuits for arithmetic:
  addition, subtraction, multiplication, division
It contains circuits for comparison and logic:
  equality, and, or, not
It contains registers: super-fast, dedicated memory connected to circuits
It contains data paths: how information flows in ALU
  from registers to circuits
  from circuits back to registers

## Slide 7: The Components of a Computer System The ALU (continued)
How to choose which operation to perform?
  Option 1: decoder signals one circuit to run
  Option 2: run all circuits, multiplexor selects one output from all circuits
In practice, option 2 is usually chosen

## Slide 9: The Components of a Computer System The ALU (continued)
How to choose which operation to perform?
  Option 1: decoder signals one circuit to run
  Option 2: run all circuits, multiplexor selects one output from all circuits
In practice, option 2 is usually chosen
Information flow:
  Data comes in from outside ALU to registers
  Signal comes to multiplexor, which operation
  Result goes back to register, and then to outside

## Slide 11: The Components of a Computer System The Control Unit
Stored program characteristic:
  Programs are encoded in binary and stored in computer’s memory
Control unit fetches instructions from memory, decodes them, and executes them
Instructions encoded:
  Operation code (op code) tells which operation
  Addresses tell which memory addresses/registers to operate on

## Slide 13: The Components of a Computer System The Control Unit (continued)
Machine language:
  Binary strings that encode instructions
  Instructions can be carried out by hardware
  Sequences of instructions encode algorithms
Instruction set:
  The instructions implemented by a particular chip
  Each kind of processor speaks a different language

## Slide 14: The Components of a Computer System The Control Unit (continued)
RISC machines and CISC machines
  Reduced instruction set computers:
    small instruction sets
    each instruction highly optimized
    easy to design hardware
  Complex instruction set computers:
    large instruction set
    single instruction can do a lot of work
    complex to design hardware
Modern hardware: some RISC and some CISC

## Slide 15: The Components of a Computer System The Control Unit (continued)
Kinds of instructions:
Data transfer, e.g., move data from memory to register
Arithmetic/Logic, e.g., add, and, etc.
Comparison, compare two values
Branch, change to a non-sequential instruction
  Branching allows for conditional and loop forms
  E.g., JUMPLT a = If previous comparison of A and B found A < B, then jump to instruction at address a

## Slide 17: The Components of a Computer System The Control Unit (continued)
Control unit contains:
Program counter (PC) register: holds address of next instruction
Instruction register (IR): holds encoding of current instruction
Instruction decoder circuit
  Decodes op code of instruction, and signals helper circuits, one per instruction
    Helpers send addresses to proper circuits
    Helpers signal ALU, I/O controller, memory

## Slide 20: Putting the Pieces Together The Von Neumann Architecture
Combine previous pieces: Von Neumann machine

## Slide 22: Putting the Pieces Together The Von Neumann Architecture
Fetch-Execute Algorithm (what the CU does)
  Address in PC is copied to MAR
  Instruction is fetched into MDR
  MDR copied to IR
  PC++
  Opcode in IR is decoded
  Operands interpreted & ALU circuits activated
  Instruction executed
  Results updated (registers, memory, PC, etc.)

## Slide 24: ALERT
Lab 8 is on Brightspace: due Wednesday
Homework #5 will be available on Brightspace and the course website on Wednesday. It is due 10/11

## Slide 25: Putting the Pieces Together The Von Neumann Architecture
Notation for computer’s behavior:
CON(A) | Contents of memory cell A
A → B | Send value in register A to register B (special registers: PC, MAR, MDR, IR, ALU, R, GT, EQ, LT, +1)
FETCH | Initiate a memory fetch operation
STORE | Initiate a memory store operation
ADD | Instruct the ALU to select the output of the adder circuit
SUBTRACT | Instruct the ALU to select the output of the subtract circuit

## Slide 26: Instruction Set for Von Neumann Machine

## Slide 27: Instruction Set for Von Neumann Machine

## Slide 28: Putting the Pieces Together The Von Neumann Architecture
LOAD X meaning CON(X) → R
  IRaddr → MAR Send address X to MAR
  FETCH Initiate Fetch, data to MDR
  MDR → R Move data in MDR to R
STORE X meaning R → CON(X)
  IRaddr → MAR Send address X to MAR
  R → MDR Send data in R to MDR
  STORE Initiate store of MDR to X

## Slide 29: Putting the Pieces Together The Von Neumann Architecture
ADD X meaning R + CON(X) → R
  IRaddr → MAR Send address X to MAR
  FETCH Initiate Fetch, data to MDR
  MDR → ALU Send data in MDR to ALU
  R → ALU Send data in R to ALU
  ADD Select ADD circuit as result
  ALU → R Copy selected result to R
JUMP X meaning get next instruction from X
  IRaddr → PC Send address X to PC

## Slide 30: Putting the Pieces Together The Von Neumann Architecture
COMPARE X meaning:
if CON(X) > R then GT = 1 else 0
if CON(X) = R then EQ = 1 else 0
if CON(X) < R then LT = 1 else 0
  IRaddr → MAR Send address X to MAR
  FETCH Initiate Fetch, data to MDR
  MDR → ALU Send data in MDR to ALU
  R → ALU Send data in R to ALU
  SUBTRACT Evaluate CON(X) – R
  Sets EQ, GT, and LT

## Slide 31: Putting the Pieces Together The Von Neumann Architecture
JUMPGT X meaning:
if GT = 1 then jump to X
else continue to next instruction
  IF GT = 1 THEN IRaddr → PC

## Slide 32: The Components of a Computer System Input/Output and Mass Storage
Input/Output (I/O) connects the processor to the outside world:
  Humans: keyboard, monitor, etc.
  Data storage: hard drive, DVD, flash drive
  Other computers: network
RAM = volatile memory (gone without power)
Mass storage systems = nonvolatile memory
  Direct access storage devices (DASDs)
  Sequential access storage devices (SASDs)

## Slide 33: The Components of a Computer System I/O and Mass Storage (continued)
DASDs
Hard drives, CDs, DVDs contain disks
  Tracks: concentric rings around disk surface
  Sectors: fixed size segments of tracks, unit of retrieval
  Time to retrieve data based on:
    seek time
    latency
    transfer time
Other non-disk DASDs: flash memory, optical

## Slide 35: The Components of a Computer System I/O and Mass Storage (continued)
DASDs and SASDs are orders of magnitude slower than RAM: (microseconds or milliseconds)
I/O Controller manages data transfer with slow I/O devices, freeing processor to do other work
Controller sends an interrupt signal to processor when I/O task is done