## Slide 1
Network Structures
Based on Dr. Pete’s adaptation of Chapter 1 of Computer Networking: A Top Down Approach, 6th edition
Jim Kurose, Keith Ross
Addison-Wesley

## Slide 2: What’s the Internet?
connected devices:
  hosts = end systems
  running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Packet switches: forward packets (chunks of data)
  routers and switches
wired
links
wireless
links
router
mobile network
global ISP
regional ISP
home
network
institutional
network
smartphone
PC
server
wireless
laptop

## Slide 3: A closer look at network structure
network edge:
  hosts: clients and servers
  servers in data centers
network access media:
  wired & wireless
  communication links
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 4: Access networks and physical media
Question: How to connect end systems to edge router?
mobile access networks
residential access nets
institutional access networks (school, company)

## Slide 5: Access net: digital subscriber line (DSL)
central office
ISP
telephone
network
voice, data transmitted
at different frequencies over
dedicated line to central office
  use existing telephone line to central office
    data over DSL phone line goes to Internet
    voice over DSL phone line goes to telephone net
  ~ 1 Mbps upload transmission rate
  ~ 10 Mbps download transmission rate
DSL
modem
splitter

## Slide 6: Access net: cable network
data, TV transmitted at different
frequencies over shared cable
distribution network
cable
modem
splitter
…
ISP
hybrid fiber-coaxial cable
  ~10 Mbps upstream transmission rate
  ~ 50Mbps download transmission rate
homes share access network to cable headend
Cable headend

## Slide 7: Access net: home network

## Slide 8: Institutional Networks
typically used in companies, universities, etc
  10 Mbps, 100Mbps, 1Gbps, 10Gbps transmission rates
  end systems typically connect into Ethernet switch
Ethernet
switch
institutional mail,
web servers
institutional router
institutional link to
ISP (Internet)

## Slide 9: Wireless access networks
shared wireless access network connects end system to router
local-area wireless access:
  within building (100 ft)
  WiFi: 54 Mbps transmit rate
wide-area wireless access
  provided by cell network, (20 mi)
  3G, 4G, 5G: 3 to 30 to 100 Mbps
to Internet
to Internet

## Slide 10: Wired physical media
coaxial cable:
two concentric copper conductors
fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
twisted pair:
two insulated copper wires

## Slide 11: Wireless physical media
Microwave
  up to 45 Mbps
WiFi
  11Mbps, 54 Mbps
Cellular
  3G: ~3 Mbps
  4G: ~30 Mbps
  5G: ~100 Mbps
Satellite
  Kbps to 45Mbps channel
  270 msec end-end delay
  geosynchronous versus low altitude

## Slide 12: The network core
mesh of interconnected routers
packet-switching: hosts break messages into packets
  forward packets from one router to the next on path from source to destination

## Slide 13: Internet structure: network of networks
End systems connect to Internet via access ISPs (Internet Service Providers)
Access ISPs in turn must be interconnected.
  So any two hosts can send packets to each other
Resulting network of networks is very complex
  Evolution was driven by economics and national policies
Let’s take a stepwise approach to describe current Internet structure

## Slide 14: Internet structure: network of networks
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 15: Analogy: National Highway System

## Slide 16: Central Ohio Highways and Roads

## Slide 17: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Tiers of Internet Service Providers (ISPs), exchange points (IXP)
ISP B
ISP A
ISP C
IXP
IXP
regional net

## Slide 18: Internet structure: network of networks
at center: small # of well-connected large networks
  tier-1 commercial ISPs (e.g., Sprint, AT&T), national & int’l coverage
  content provider network (e.g, Google): private network that connects its data centers to Internet, often bypassing tier-1, regional ISPs
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Regional ISP
Regional ISP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
IXP