## Slide 1
Circuits & Functional Components

## Slide 2: ALERTs
Assignment 4 is available on Brightspace and is due Friday (2/6)
The first midterm is Friday, February 27
  It will cover chapters 1-4

## Slide 3: Building Computer Circuits
Full adder circuit
Input is two unsigned N-bit numbers
Output is one unsigned N-bit number, the result of adding inputs together
Example:
Start with one-bit adder (1-ADD)
 |  |  |  | 1 | 
 | 0 | 0 | 1 | 0 | 1
+ | 0 | 1 | 0 | 0 | 1
 | 0 | 1 | 1 | 1 | 0

## Slide 4
Single bit adder

## Slide 5: Building Computer Circuits
Sum digit, si, has Boolean expression:
  (~ai  ~bi  ci) + (~ai  bi  ~ci) + (ai  ~bi  ~ci) + (ai  bi  ci)
Carry digit, ci+1, has Boolean expression:
  (~ai  bi  ci) + (ai  ~bi  ci) + (ai  bi  ~ci) + (ai  bi  ci)

## Slide 6
Single bit adder
si = (~ai  ~bi  ci) + (~ai  bi  ~ci) + (ai  ~bi  ~ci) + (ai  bi  ci)
ci+1 =(~ai  bi  ci) + (ai  ~bi  ci) +
(ai  bi  ~ci) + (ai  bi  ci)

## Slide 7: Building Computer Circuits
N-bit adder circuit
Input: a0a2…an-1 and b0b2…bn-1, where ai and bi are individual bits
a0 and b0 are least significant digits: ones place
Pair up corresponding bits: a0 with b0, a1 with b1, etc.
Run 1-ADD on a0 and b0, with fixed carry in c0 = 0
Feed carry out c1 to next 1-ADD and repeat

## Slide 8
N-bit adder

## Slide 9: Control Circuits
Control circuits make decisions, determine order of operations, select data values
Multiplexor selects one from among many inputs
  2N input lines
  N selector lines
  1 output line
Each input line corresponds to a unique pattern on selector lines
That input value is passed to output

## Slide 10
2-1 MUX & 4-1 MUX

## Slide 11: Control Circuits
Decoder sends a signal out only one output, chosen by its input
  N input lines
  2N output lines
Each output line corresponds to a unique pattern on input lines
Only the chosen output line produces 1, all others output 0

## Slide 12
2-4 & 3-8 Decoders

## Slide 13: Control Circuits
Decoder circuit uses
  To select a single arithmetic instruction, given a code for that instruction
  Code activates one output line, that line activates corresponding arithmetic circuit
Multiplexor circuit uses
  To choose one data value from among a set, based on selector pattern
  Many data values flow into the multiplexor, only the selected one comes out

## Slide 15: Memory Circuits
The circuits we've seen so far have all be examples of what are called combinatorial circuits
  These perform computations that are functions of inputs to outputs
  These kinds of circuits can't be used to store data, since they are feeding signals in a forward path through the electronics
Sequential circuits are designed to store bits (0s and 1s) over time, so support operations that store and fetch
  Storing a 1 is called 'set'
  Storing a 0 is called 'reset'
  An SR-Flip Flop is a circuit that implements this idea

## Slide 16: SR-Flip Flop
S R | Q Q’
0 0 1 0 0 1 1 1 | Q Q’ 0 0 1 0 0
S R | Q Q’
1 1 0 1 1 0 0 0 | Q Q’ 0 0 1 1 1
RESET
SET
SET
RESET

## Slide 17: Memory Functions
Fetch: retrieve from memory (nondestructive)
Store: write to memory (destructive)
Memory access time
  time required to fetch/store
  Modern RAM requires 5-10 nanoseconds
MAR holds memory address to access
MDR receives data from fetch, holds data to be stored

## Slide 18: Accessing Memory
Memory system circuits: decoder and fetch/store controller
Decoder converts MAR into signal to a specific memory cell
  One-dimensional versus two-dimensional memory organization
Fetch/Store controller = traffic cop for MDR
  Takes in a signal that indicates fetch or store
  Routes data flow to/from memory cells and MDR

## Slide 19
Decoding Memory Addresses

## Slide 20
2D Memory
In practice it is more efficient to organize memory as a 2D grid rather than a 1D array
The memory addresses can then be split in half and independently fed to two decoders that will have significantly smaller logic circuits
Why is this the case?